## Slide 1
A PRESENTATION ON Weather Monitoring and Remote Plant Watering system using ESP32 and Blynk Live Server and App
Department of Electronics and Telecommunication Engineering
Chittagong University of Engineering and Technology
COURSE CODE: ETE-416
COURSE TITLE: IoT and Industrial Automation Sessional
PRESENTED BY:
Group-3 (ID: 1708011, 1708012, 1708013, 1708014, 1708015)

## Slide 2
OUTLINE
      INTRODUCTION
      SIMULATION
      CODE
      HARDWARE IMEPLEMENTATION
      RESULT
      CONCLUSION
      FUTURE DIRECTION

## Slide 3
INTRODUCTION
1
In Today’s World of agriculture, knowing live environmental condition and take recountable actions or precautions is one of the biggest issues for farmers and agriculturist.
In this project, a remote weather monitoring and plant watering system is designed which will reduce human workload and interference in agricultural activity.

## Slide 4
INTRODUCTION(CONT’D)
2
BLYNK
CLOUD
Sensor Data
ESP32
DHT11
Relay Module
DC Motor
Sensor Data
Sensor Data
Motor Control Signal
Control
Signal
Trigger
Signal
Figure 01: Working Diagram of Weather Monitoring and Remote Plant Watering System

## Slide 5
SIMULATION
3
Figure 02: Proteus Schematic Design

## Slide 6
CODE
The code for this project is given below:
#define BLYNK_PRINT Serial
#define BLYNK_TEMPLATE_ID "TMPLQNF8LYfz"
#define BLYNK_DEVICE_NAME "Weather Monitoring and Plant Watering System"
#include <WiFi.h>
#include <WiFiClient.h>
#include <BlynkSimpleEsp32.h>
#include "DHT.h"
char auth[] = "******"; // auth token
char ssid[] = "******"; //wifi name
char pass[] = "******"; // wifi password
#define DHTPIN 2
#define DHTTYPE DHT11
DHT dht(DHTPIN, DHTTYPE);
BlynkTimer timer;
bool Relay = 0;
#define waterPump 26
void sendSensor()
{
float h = dht.readHumidity();
float t = dht.readTemperature();
4

## Slide 7
CODE(CONT’D)
if (isnan(h) || isnan(t)) {
Serial.println("Failed to read from DHT sensor!");
return;
}
Blynk.virtualWrite(V1, h);
Blynk.virtualWrite(V0, t);
}
void setup()
{
Serial.begin(115200);
delay(1000);
pinMode(waterPump, OUTPUT);
digitalWrite(waterPump, HIGH);
Blynk.begin(auth, ssid, pass, "blynk.cloud", 80);
dht.begin();
timer.setInterval(1000L, sendSensor);
}
5

## Slide 8
CODE(CONT’D)
void loop()
{
Blynk.run();
timer.run();
}
BLYNK_WRITE(V2) {
Relay = param.asInt();
if (Relay == 1) {
digitalWrite(waterPump, LOW);
Serial.println("Motor On");
} else {
digitalWrite(waterPump, HIGH);
Serial.println("Motor Off");
}
delay(5000);
}
6

## Slide 9
HARDWARE IMPLEMENTATION
7
Figure-03: Prototype Design of the proposed model

## Slide 10
HARDWARE IMPLEMENTATION(CON’T D)
8
IoT Fundamental Stack has three layer
        Application Layer
        Communication Networks Layer
        Things: Sensors and Actuators

## Slide 11
HARDWARE IMPLEMENTATION(CON’T D)
9
Application Layer is implemented using Blynk Live server.
Communications Network layer is implemented using ESP32 microcontroller.
In Things: Sensors and Actuator layer, DHT11 was used as sensor and DC motor as actuator.

## Slide 12
HARDWARE IMPLEMENTATION(CON’T D)
10
(a) Web Dashboard
(b) Mobile Dashboard
Figure-04: Blynk Live Server Configuration

## Slide 13
RESULT
11
Obs. No. | Heat Source | Reading (°C) |  | Delay (s)
 |  | Before Giving Heat | After Giving Heat | 
01. | Candle | 22.08 | 22.15 | 7s
02. | Match | 23.60 | 23.62 | 16s
03. | Sunlight | 23.40 | 23.45 | 12s
Observation No. | Reading (%) |  | Delay(s)
 | Before GivingWater | After GivingWater | 
01. | 64.00 | 65.20 | 11s
02. | 70.20 | 73.65 | 7s
03. | 65.60 | 69.45 | 4s
Table-01: Temperature Sensor Response Time Observation
Table-02: Humidity sensor Response
Time Observation

## Slide 14: RESULT(CONT’D)
(a) For Temperature
(b) For Humidity
Figure-04: Relation between Response and Deviation in Measurement
12

## Slide 15
RESULT(CONT’D)
13
Table-03: Temperature sensor
Accuracy Measurement
Table-04: Humidity sensor
Accuracy Measurement
Obs. No. | Measure by Mobile App(°C) | Measured by DHT11 (°C) | Accuracy (%)
01. | 23.59 | 24.20 | 97.41%
02. | 21.65 | 22.50 | 96.07%
03. | 22.59 | 22.85 | 98.84%
Obs. No. | Measuredby Mobile App (%) | Measured by DHT11 (%) | Accuracy (%)
01. | 53.62% | 51.43% | 95.92%
02. | 57.37 | 59.97 | 95.47%
03. | 64.60 | 65.54 | 98.54%

## Slide 16
CONCLUSION
14
This project achieved the objectives to build a weather monitoring and remote plant watering system
The project has the potential to be implemented for monitoring the developing cities and industrial zones, especially for pollution monitoring

## Slide 17
FUTURE DIRECTION
15
This project can be extended to automate many aspect of an agricultural system by using multiple sensor.
This sensor data can be used by experts to predict any sudden change in weather and take precautionary steps such as inventing new plants and cultivation system.